AX-TOOLBOX
Flight Analysis Scripting Language
# Introduction
## Language basics
The flight analysis scripting language have two kind of instructions: settings and object constructors. The settings are used to set up some program options and variables and the constructors are used to define the flight tasks.
### Settings
The setting instructions have the following syntax:
SET <key> = <one or more values>
The distinct values are separated by commas.
### Constructors
The constructor instructions have the following syntax:
<class> <name> = <type>(<zero or more parameters>)
The distinct parameters are separated by commas.
### Comments and blank characters
Any line whose first non space characters are double slashes '//' will be ignored. All blank lines are also ignored as well as all blank characters (spaces or tabs) before or after any symbol (instruction, name, key, type, value or parameter).
## Notation Conventions
### Names
Names can be any sequence of characters. All characters are allowed except commas ','.
### Distances and altitudes
Distance and altitude definitions are double precision floating point numbers with dot '.' decimal separator. The known units of measure are meters 'm', kilometers 'km', feet 'ft', miles 'mi' or nautical miles 'nm'.
Examples:
500m
1640.42ft
### Time definitions
Time definitions are in the format 'HH:MM:SS' (hours, minutes and seconds). The seconds part is optional. Applies to absolute times (time of day) as well to relative times (time span).
Examples:
10:30:00
10:30
### Colors
Only the following colors are allowed: blue, brown, gray, green, orange, pink, red, violet, white and yellow.
# SET instruction
SET <key> = <value>[, <value>...]
Allows to set different options.
## Definition
### Key DATETIME: flight date and time
set DATETIME = <date>, <time>
Sets the flight date and time
<date> is the flight date in format yyyy/mm/dd
<time> is either AM or PM
### Key DATUM
set DATUM = <datumName>
Sets the default datum.
<datumName> is the datum name
Supported datums: Corrego Alegre, European 1950, NAD27 CONUS, OSGB36, WGS72, WGS84.
### Key UTMZONE
set UTMZONE = <zone>
Sets the default UTM zone.
<zone> is the UTM zone
### Key QNH
set QNH = <value>
Sets the QNH value
<value> is the qnh value
### Key DRATHRESHOLD
set DRATHRESHOLD = <value>
Sets the threshold for relative altitude distance computations. If the altitude difference between two points is less than the threshold, 2D distance will be computed. Otherwise, 3D distance is used. If undefined, 0m is assumed (always distance in 3D).
<value> is the threshold value
### Key DEFAULTALTITUDE
set DEFAULTALTITUDE = <altitude>
Sets the default altitude for pilot declared goals. If undefined, 0 MSL will be assumed.
<altitude> is the default altitude
### Key MAXDISTTOCROSSING
set MAXDISTTOCROSSING = <distance>
Sets the maximum allowed distance from a pilot declared goal to a valid road crossing. If undefined, 200m will be assumed.
<distance> maximum allowed distance
### Key SMOOTHNESS
set SMOOTHNESS = <value>
Sets the smoothness factor (moving average values) used in automatic launch and landing detection. If undefined, 3 will be assumed.
<value> is the smoothness factor
### Key MINSPEED
set MINSPEED = <speed>
Sets the minimum speed (in m/s) considered as movement in automatic launch and landing detection. If undefined, 0.5 will be assumed.
<speed> is the minimum speed
### Key MAXACCELERATION
set MAXACCELERATION = <acceleration>
Sets the maximum acceleration (in m/s^2) allowed in normal flight. Track points with greater acceleration will be discarded as bogus (spikes). If undefined, 0.3 will be assumed.
<acceleration> is the maximum acceleration
## Examples
set DATETIME = 2010/09/19, AM
set DATUM = European 1950
set QNH = 1013
set MINSPEED = 0.3
set MAXDISTTOCROSSING = 300m
# MAP class
MAP <mapName> = <mapType>(<map params>)
There must be one and only one map file per script. If more than one is defined, only the last is used. The area covered by the map is assumed to be the competition area.
## Constructors
<mapType>(<map params>)
### Type BITMAP: Bitmap file
BITMAP(<fileName>)
<fileName> is a bitmap file name. Compatible bitmap types are bmp, gif, jpg, png, tif. A corresponding world file must exist. See http://en.wikipedia.org/wiki/World_file for more information.
### Type BLANK: Blank map
Blank(<topLeft>, <bottomRight>)
<topLeft> is a previously defined point name designing the top-left corner of the map.
<bottomRight> is a previously defined point name designing the bottom-right corner of the map.
## Display modes
<displayMode>(<display params>)
### Mode GRID
GRID(<width>)
<width> is the desired grid spacing between lines.
Draws a grid over the map.
## Examples
MAP CompetitionMap = BITMAP(map.png) grid(1000)
MAP OfficialMap = Blank(TopLeftPoint,BottomRightPoint)
# TASK class
TASK <taskName> = <taskType>()
<taskType> is one of the AXMER allowed task type.
## Constructors
<taskType>()
### PDG - Pilot Declared Goal
PDG()
### JDG - Judge Declared Goal
JDG()
### HWZ - Hesitation Waltz
HWZ()
### FIN - Fly In
FIN()
### FON - Fly On
FON()
### HNH - Hare And Hounds
HNH()
### WSD - Watership Down
WSD()
### GBM - Gordon Bennett Memorial
GBM()
### CRT - Calculated Rate Of Approach
CRT()
### RTA - Race To An Area
RTA()
### ELB - Elbow
ELB()
### LRN - Land Run
LRN()
### MDT - Minimum Distance
MDT()
### SFL - Shortest Flight
SFL()
### MDD - Minimum Distance Double Drop
MDD()
### XDT - Maximum Distance Time
XDT()
### XDI - Maximum Distance
XDI()
### XDD - Maximum Distance Double Drop
XDD()
### ANG - Angle
ANG()
### 3DT - 3D Shape Task
3DT()
## Examples
TASK Task3HWZ = HWZ()
TASK Task2 = JDG()
# AREA class
AREA <name> = <areaType>(<area params>) [<displayMode>(<display params>)]
## Constructors
<areaType>(<area params>)
### Type CIRCLE: Circular area
CIRCLE(<center>, <radius>)
<center> is a point name used as the circle center
<radius> is the circle radius
### Type POLY: Polygonal area
POLY(<fileName>)
<fileName> is the name of a track file containing the polygon (trk, igc)
## Display modes
<displayMode>(<display params>)
The display mode is optional. If it is not specified, DEFAULT(blue) is used.
### Mode NONE
NONE()
The area will not be displayed.
### Mode DEFAULT
DEFAULT([<color>])
Draws the area according to its type.
<color> is one of blue, brown, gray, green, orange, pink, red, violet, white, yellow. If no color is specified, blue will be used.
## Examples
area Area1 = CIRCLE(P10, 100) DEFAULT(green)
area Area2 = POLY(area2.trk)
area Area3 = CIRCLE(P10, 500) NONE()
# FILTER class
Filter track points for the current task. Points filtered out are not considered in further computations. Successive filters in the same task are applied in definition order.
FILTER <name> = <filterType>(<filter params>)
## Constructors
### INSIDE
INSIDE(<areaName>)
Selects all the track points inside the specified area.
<areaName> is the name of a previously defined area
### OUTSIDE
OUTSIDE(<areaName>)
Selects all the track points outside the specified area.
<areaName> is the name of a previously defined area
### BEFORETIME
BEFORETIME(<time>)
Selects all the track points earlier than specified time.
<time> desired time in hh:mm:ss
### AFTERTIME
AFTERTIME(<time>)
Selects all the track points later than specified time.
<time> desired time in hh:mm:ss
### BEFOREPOINT
BEFOREPOINT(<pointName>)
Selects all the track points earlier than specified point.
<pointName> is the name of a previously defined point
### AFTERPOINT
AFTERPOINT(<pointName>)
Selects all the track points later than specified point.
<pointName> is the name of a previously defined point
### ABOVE
ABOVE(<altitude>)
Selects all the track points above a given altitude
<altitude> is the desired altitude limit in feet
### BELOW
BELOW(<altitude>)
Selects all the track points below a given altitude
<altitude> is the desired altitude limit in feet
### NONE
NONE()
Clears all the active filters for the current task. Previous computations are not affected.
## Examples
FILTER InArea = INSIDE(GBMArea)
FILTER Before10:00 = BEFORETIME(10:00:00)
# POINT class
POINT <name> = <pointType>(<point params>) [<displayMode>(<display params>)]
## Static point (S) constructors
The S constructors return a statically defined point.
### Type SLL: WGS84 lat/long
SLL(<lat>, <long>, <altitude>)
Returns a statically defined point using WGS lat/lon coordinates.
<lat> is the latitude coordinate
<long> is the longitude coordinate
<altitude> is the altitude (in feet)
### Type SUTM: UTM
SUTM(<easting>, <northing>, <altitude>)
Returns a statically defined point using UTM coordinates in the default datum and zone.
<easting> is the easting coordinate
<northing> is the northing coordinate
<altitude> is the altitude (in feet)
## Point from a list (L) constructors
The L constructors return a point chosen form a list of predefined points.
### Type LNP: nearest to point
LNP(<desiredPoint>, <listPoint1>, <listPoint2>, ...)
Returns the point closest to a desired one from a list of predefined points.
### Type LFT: first in time
LFT(<listPoint1>, <listPoint2>, ...)
Returns the earliest point from a list of points.
### Type LLT: last in time
LLT(<listPoint1>, <listPoint2>, ...)
Returns the latest point from a list of points.
### Type LFNN: first not null
LFNN(<listPoint1>, <listPoint2>, ...)
Returns the first non null point from a list of points.
### Type LLNN: last not null
LLNN(<listPoint1>, <listPoint2>, ...)
Returns the last non null point from a list of points.
## Logger mark (M) constructors
The M constructors return a point defined with a logger mark.
### Type MVMD: virtual marker drop
MVMD(<number>)
Returns the first occurrence of the desired virtual marker drop. The filters applied to track points are enforced because virtual marker drops must coincide with a valid track point.
<number> desired marker number
### Type MPDG: pilot declared goal
MPDG(<number>, <minTime>, <maxTime>)
Returns the last occurrence of the desired pilot declared goal within time limits.
<number> desired pilot declared goal number
<minTime> declaration lower time limit
<maxTime> declaration upper time limit
## Track point (T) constructors
The T constructors return a point from the track log.
### Type TLCH: launch
TLCH()
Returns the launch point.
### Type TLND: landing
TLND()
Returns the landing point.
### Type TNP: nearest to point
TNP(<pointName>)
Returns the closest valid track point to the specified point.
<pointName> is the name of a previously defined point
### Type TNL: nearest to point list
TNL(<listPoint1>, <listPoint2>, ...)
Returns the closest valid track point to any the specified points.
<listPoint> is the name of another previously defined point
### Type TDT: delayed in time
TDT(<pointName>, <timeDelay>[, <maxTime>])
If <maxTime> is not specified, returns the first valid track point after <timeDelay> minutes have elapsed over the desired point time.
If <maxTime> is specified, returns the last valid track point after <timeDelay> minutes have elapsed over the desired point time but before <maxTime>.
<pointName> is the name of another previously defined point
<timeDelay> desired time delay in minutes
<maxTtime> desired time limit. This parameter is optional
### Type TDD: delayed in distance
TDD(<pointName>, <distanceDelay>[, <maxTime>])
If <maxTime> is not specified, returns the first valid track point farther than <distanceDelay> from the desired point.
If <maxTime> is specified, returns the last valid track point before <maxTime> farther than <distanceDelay> from the desired point.
<pointName> is the name of another previously defined point
<distanceDelay> desired distance delay in meters
<maxTime> desired time limit. This parameter is optional
### Type TAFI: area first in
TAFI(<areaName>)
Returns the first valid track point after entering the area for the first time.
<areaName> is the name of a previously defined area
### Type TAFO: area first out
TAFO(<areaName>)
Returns the last valid track point before exiting the area for the first time.
<areaName> is the name of a previously defined area
### Type TALI: area last in
TALI(<areaName>)
Returns the first valid track point after entering the area for the last time.
<areaName> is the name of a previously defined area
### Type TALO: area last out
TALO(<areaName>)
Returns the last valid track point before exiting the area for the last time.
<areaName> is the name of a previously defined area
## Display modes
<displayMode>(<display params>)
The display mode is optional. If it is not specified, WAYPOINT(blue) is used.
### Mode NONE
NONE()
The point will not be displayed.
### Mode WAYPOINT
WAYPOINT([<color>])
Displays a waypoint map overlay.
<color> is one of blue, brown, gray, green, orange, pink, red, violet, white, yellow. If no color is specified, blue will be used.
### Mode TARGET
TARGET(<radius>[, <color>])
Displays a target map overlay with a circular area of given radius.
<radius> circular area radius in meters.
<color> is one of blue, brown, gray, green, orange, pink, red, violet, white, yellow. If no color is specified, blue will be used.
### Mode MARKER
MARKER([<color>])
Displays a flag map overlay.
<color> is one of blue, brown, gray, green, orange, pink, red, violet, white, yellow. If no color is specified, blue will be used.
### Mode CROSSHAIRS
CROSSSHAIRS([<color>])
Displays a crosshairs map overlay.
<color> is one of blue, brown, gray, green, orange, pink, red, violet, white, yellow. If no color is specified, blue will be used.
## Examples
point LAUNCH = TLCH() WAYPOINT(green)
point LANDING = TLND() WAYPOINT(red)
point G12 = SLL(42.12, 3.23, 1500) TARGET(100, green)
point G13 = SUTM(31T, 235123, 4612153, 850) TARGET(100, green)
point Best = TNL(G12, G13) MARKER(green)
# RESULT class
RESULT <resultName> = <resultType>(<result params>)
Computes a task result. The results are assigned to the last defined task.
## Constructors
<resultType>(<result params>)
### Type D2D: distance in 2D
D2D(<pointNameA>, <pointNameB>)
Computes the projected distance (in 2D) between two points.
### Type D3D: distance in 3D
D3D(<pointNameA>, <pointNameB>)
Computes the distance in 3D between two points.
### Type DRAD: relative altitude dependent distance
DRAD(<pointNameA>, <pointNameB>)
Computes the distance between two points. If the altitude difference between the two is less than the threshold specified in the settings part, 2D distance will be computed. Otherwise, 3D distance is used.
### Type DACC: accumulated distance
DACC(<pointNameA>, <pointNameB>)
Computes the sum of the distances between consecutive valid track points from point 1 to point 2. In other words, It computes the total traveled distance between the two points.
### Type TSEC: time in seconds
TSEC(<pointNameA>, <pointNameB>)
Computes the time elapsed in seconds between the two points.
### Type TMIN: time in minutes
TMIN(<pointNameA>, <pointNameB>)
Computes the time elapsed in minutes between the two points.
### Type ATRI: area of triangle
ATRI(<pointNameA>, <pointNameB>, <pointNameC>)
Computes the area in km2 of the triangle delimited by the three points.
### Type ANG3P: angle between 3 points
ANG3P(<pointNameA>, <pointNameB>, <pointNameC>)
Computes the direction change between AB and BC (180 - the angle ABC).
### Type ANGN: angle to the north
ANGN(<pointNameA>, <pointNameB>)
Computes the angle between the line AB and the line north-south.
### Type ANGSD: angle to a set direction
ANGSD(<pointNameA>, <pointNameB>, <setDirection>)
Computes the angle between the line AB and a set direction. 0 is north-south.
## Examples
RESULT Task3Result=DRAD(Task3Marker,Task3Target,500)
# Full task examples
## Judge Declared Goal (nearest track point)
TASK Task02JDG = JDG()
POINT Task02target=UTM(31T,325000,4612000,650)
FILTER Task02scoringPeriod1=AFTER(09:00:00)
FILTER Task02scoringPeriod2=BEFORE(10:00:00)
POINT Task02marker=TNP(Task02target)
RESULT Task02result=DRAD(Task02target,Task02marker,500)
The first line defines the task type, JDG. The second line defines the target. The next two lines define the scoring period from 9:00 to 10:00. The fifth line defines the nearest track point to the target. The last line computes the result, a relative altitude dependent distance with an altitude limit of 500ft.
## Hesitation Waltz (logger marker drop)
TASK Task03HWZ=HWZ()
POINT Task03t1=UTM(31T,325000,4612000,650)
POINT Task03t2=UTM(31T,325500,4612000,650)
POINT Task03t3=UTM(31T,325000,4612500,650)
POINT Task03marker=MVMD(3)
POINT Target=LNP(Task03marker,Task03t1,Task03t2,Task03t3)
RESULT Result=D3D(Marker,Target)
The first line defines the task type, HWZ. The next three lines define the targets. The fifth line defines the logger marker drop #3. The sixth line defines the closest target to the marker. The last line computes the result, a distance in 3D.
## Gordon Bennett Memorial (logger marker drop)
TASK Task1=GBM()
AREA T1area=Area(task1area.trk)
POINT T1goal=SUTM(31T,3166732,4613455,350)
FILTER T1scoringPeriod=BEFORE(10:00:00)
POINT T1marker=MVMD(1)
RESULT=DRAD(T1Goal,T1marker,500)
The first line defines a GBM task. The second line defines the scoring area from a track file. The third line defines the goal, a fixed UTM point. The next line defines a scoring period until 10:00. The next defines the logger marker #1 (note that the scoring period filter also applies to VMDs). The last line computes a relative altitude dependent distance with a threshold of 500ft.
## Maximum Distance Double Drop (first in / last out)
TASK Task4=XDD()
AREA T4area=Area(task4area.trk)
FILTER T4scoringPeriod=BEFORE(10:00:00)
POINT T4A=TAFI(T4area)
POINT T4B=TALO(T4area)
RESULT t4result=D2D(T4A,T4B)
The first line defines the task type, XDD. The second line defines the task area from a track file. The third line applies a filter: the valid track points are those before 10:00:00 (task scoring period up to 10:00). The next line defines the first scoring point, the first-in point. The next defines the second scoring point, the last-out point. The last line computes the result, a distance in 2D.
# Bugs and ideas
The point constructors LNP, TNP and TNL do not specify what kind of distance should be used (d2d, d3d or drad). Consider constructors that specify the distance method.
Example: LNPD2D, LNPD3D, LNPDRAD, TNPD2D, TNPD3D, TNPDRAD, etc.
Think about a method to score a 3DS task allowing entering and exiting the area multiple times.